## Slide 1
Kong Chyong
Cambridge Judge Business School
University of Cambridge
2022 CEEPR & EPRG International Energy Policy Conference
Brussels
1 Sept 2022
Russia’s invasion of Ukraine: medium-term implications for European and global gas markets

## Slide 2
2
Key questions
How might we see global energy supply and demand evolve with a prolonged shut down of Russian gas to Europe?
Will new sources of gas come on stream to replace lost Russian volumes?

## Slide 3
3
Q1: How might we see global energy supply and demand evolve with a prolonged shut down?
It takes more than a decade to ramp up production to replace Russian gas;
Analysis of future LNG projects, their economics, potential security of supply issues and contractual models that would fit with European decarbonization narratives;
Outlook for LNG demand (non-Europe) and its price responsiveness.

## Slide 4
4
Ramping up LNG exports takes time
Source: BP (2021); Eikon Terminal
Chart: bcm/yr
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
Qatar | 14.4743 | 17.4731 | 19.0787 | 19.4258 | 24.8285 | 28.4879 | 33.4651 | 39.6497 | 41.0581 | 51.7542 | 77.825 | 100.7102 | 104.0101 | 105.8204 | 103.607 | 105.619 | 107.3023 | 103.5756 | 104.9461 | 105.8149 | 106.0846
Australia | 10.2563 | 10.4068 | 10.5007 | 10.6509 | 12.1879 | 15.4598 | 19.1352 | 20.8969 | 20.8876 | 25.1336 | 25.8363 | 26.0169 | 28.2932 | 30.5199 | 32.0335 | 39.9142 | 60.3857 | 76.5506 | 91.8197 | 104.655 | 106.2315
US | 1.6988 | 1.7507 | 1.7794 | 1.6977 | 1.7025 | 1.9259 | 1.6171 | 1.2372 | 1.0114 | 0.81792 | 1.4502 | 1.7506 | 0.77573 | 0.15287 | 0.42522 | 0.69486 | 4.021 | 17.1257 | 28.575 | 47.4025 | 61.3944
US expansion still ongoing (Cheniere/Sabine Pass T1 started in 2016)
Reminder: Russian gas to Europe is ca. 155 bcm (2021)

## Slide 5
5
Global LNG capacity addition and demand growth by 2025
Source: Eikon terminal
IEA’s most recent (Jul-22) incremental LNG demand assessment

## Slide 6
6
Global LNG capacity addition and demand growth by 2025
Source: Eikon terminal
IEA’s most recent (Jul-22) incremental LNG demand assessment
RU Artic T2 won’t come online due to sanctions
Qatari LNG expansion timeline too ambitious

## Slide 7
7
Global LNG capacity addition and demand growth by 2025
Source: Eikon terminal
IEA’s most recent (Jul-22) incremental LNG demand assessment

## Slide 8
8
Global LNG capacity (derated) addition and demand growth by 2025
Source: Eikon terminal
IEA’s most recent (Jul-22) incremental LNG demand assessment

## Slide 9
9
Price impacts on gas demand forecasts
Source: IEA (2022)

## Slide 10
10
LNG contracts signed in 2021&H1-22
Source: IEA (2022)
Europe + Portfolio = ca. 50 bcm, or 32% of RU gas export (2021).

## Slide 11
11
LNG contracts signed in 2021&H1-22
Source: IEA (2022)
IEA analysis implies that on top of additional measures European utilities will need to contract with IOCs for the flex LNG volume & buys spot cargoes

## Slide 12
12
Q2: Will new sources of gas come on stream to replace lost RU volumes?
Yes, LNG is in abundance but requires long-term contracts (volume guarantee for banks to finance these projects);
Contractual models that would fit with European decarbonization narratives while keeping gas prices stable and competitive enough to refuel European (i.e., German) industry;
More important question – when and with what capacity will (if ever) Russia come back to the global energy markets?

## Slide 13
13
Non-FID LNG projects (bcm/y)
Reminder: Russian gas to Europe is ca. 155 bcm (2021)
Source: Eikon terminal

## Slide 14
14
Non-FID LNG projects (bcm/y)
Reminder: Russian gas to Europe is ca. 155 bcm (2021)
Source: Eikon terminal

## Slide 15
15
Russia’s pivot to Asia & global LNG
Source: IEA (2022)
For this to happen, we need a geopolitical settlement between Russia, Europe and USA akin to the Yalta Conference of 1945

## Slide 16
16
Some concluding remarks/questions
A systematic cost-benefit analysis of industrial DSR capability and costs against the notion of “protected customers” under the EC gas SoS regulation is required ASAP.
What gas-based industrial processes can we replace (electrify and/or decarbonize with H2) quickly and at what cost?
How many heat pumps between now and 2030 can we install in residential buildings?